Material Safety Data Sheet					HMIS(

|  | HEALTH FLAMMABILITY | 1 3 | REACTIVITY PERSONAL PROTECTION | 0 None |
| --- | --- | --- | --- | --- |
| Identity (As Used on Label and List) 90723 No-Sweat - All Purpose Gym Wiper | Note: Blank spaces are not permitted. If any item is not applicable, or no information is available, the space must be marked to indicate that. |
| SECTION 1: Company Identification |  |
| Manufacturer's Name ITW Dymon | Emergency Telephone Number 1-800-535-5053 - Infotrac |
| Address (Number, Street, City, State, and ZIP Code) 805 East Old 56 Highway | Telephone Number for Information 1-800-323-0779 -Ricmar |
| Olathe, Kansas 66061 | Date Prepared March 22, 2006 |
| Distributed by Ricmar Industries 889 N. Larch Avenue Elmhurst, IL 60126 800-323-0779 | Signature of Preparer (Optional) Regulatory Dept. |
| SECTION 2: Ingredients/Identity Information |
| Components (Chemical Identity, |  |  |  | Other Limits |  |
| Common Name(s)) | CAS No. | OSHA PEL | ACGIH-TLV | Recommended | % (Opt.) |
| Isopropyl Alcohol | 67-63-0 | 400 ppm | 400 ppm | STEL 500 ppm | 10- 30 % |
| Any substance listed as hazardous by the States of California, Florida, Illinois, Michigan, New Jersey, Ohio, Pennsylvania or |
| Texas is described above if known present in regulated concentrations. |
| SECTION 3: Hazards Identification |
| Route(s) of Entry | Eyes? | Yes | Inhalation? | Yes | Skin? | Yes | Ingestion? | No |
| Acute Health Hazards - Warning. Flammable vapor. May cause eye or skin irritation. May cause respiratory and gastrointestinal tract irritation. Overexposure to vapors may induce central nervous system effects. |
| Chronic Health Hazards - Repeated or prolonged occupational overexposure may cause dermatitis or induce Painters Syndrome. |
| Carcinogenicity: |  |  |  |
| OSHA: No | ACGIH: No | NTP: No | IARC: No |
| Signs and Symptoms of Exposure - Redness, tearing, swelling or burning in eyes. Redness drying or cracking of the skin. Headache, drowsiness, dizziness, fatigue, loss of coordination. |
| Medical Conditions Generally Aggravated by Exposure - Pre-existing skin, lung, kidney and liver disorders may be adversely affected. Follow good chemical hygiene practices when using this product. |
| SECTION 4: Emergency and First Aid Procedures: |
| Eyes - Flush with plenty of water for at least 15 minutes lifting eyelids to insure complete removal. See a physician immediately. |
| Ingestion – Do not induce vomiting unless directed to do so by a physician. Never give anything by mouth to an unconscious person. Call a physician or poison control center immediately. |
| Inhalation - Get to fresh air. If breathing has stopped, qualified personnel should administer artificial respiration. |
| Skin - Flush with plenty of water for at least 15 minutes. If irritation arises and persists, call a physician. |
| SECTION 5: Fire Fighting Measures |
| Flash Point Concentrate (Method Used) 75o F (PMCC) | Flammable Limits No Data | LEL No Data | UEL No Data |
| Extinguishing Media - Use carbon dioxide, dry chemical, halon, polar or alcohol foam. Water may be ineffective. |
| Special Fire Fighting Procedures - Keep adjacent containers cool and vapors down with water spray. Prevent runoff from entering sewers and public waterways. Wear SCBA in chemical fires. |
| Hazardous Products of Combustion- Carbon dioxide, carbon monoxide, various hydrocarbons and soot. |
| Unusual Fire and Explosion Hazards – Usually none, but if a large amount of concentrate is released treat as a flammable liquid that may be ignited by heat, sparks, flame, static electricity, pilot lights, etc. Vapors may travel considerable distances to an ignition source then ignite, flashback or explode. |
| SECTION 6: Accidental Release Measures |
| Small Spill - Wipe up small releases with a dry absorbent cloth or other absorbent material. |
| Large Spill – Absorb liquid with vermiculite, absorbent cloth, or other absorbent material. Prevent material from entering sewers or drains. Ventilate area and block traffic. Transfer contaminated material into suitable container for proper disposal. |
| SECTION 7: Handling and Storage |
| Handling - Do not get in eyes. Avoid inhaling mist or vapors. Do not intentionally concentrate and inhale vapors. Do not swallow. Do not use or store around ignition sources such as heat, sparks, flame, static electricity, pilot lights, etc. Do not smoke while using. Wash thoroughly after handling. |
| Storage – Follow label directions carefully. Keep out of reach of children. Keep container tightly sealed when not in use. Do not contaminate water, food, or feed by use or storage. Empty container may retain flammable vapors. Keep from freezing. Store in a cool well ventilated area. Keep away from heat sources. |
| SECTION 8: Exposure Controls / Personal Protection |
| Eye Protection – Not usually necessary. Only if direct contact is possible. Use approved safety glasses (ANSI Z87) or goggles. |
| Skin Protection – Not usually necessary. |
| Respiratory Protections – Not usually necessary. Use with adequate ventilation. Use NIOSH/MSHA approved respirator if PELs or TLVs are exceeded. |
| Engineering Controls – Ventilation not usually necessary but should be provided in the event of overexposure. |
| SECTION 9: Physical and Chemical Properties |
| Appearance and Odor: | Hazy white translucent liquid on a towel with an alcohol -cumcumber scent. |
| Physical State: | Liquid impregnated towel. |
| PH | 6.7 + 0.5 |
| Specific Gravity (70oF) | 0.968 |
| Boiling Point: | 212o F |
| Melting Point: | No Data |
| Evaporation Rate (Butyl Acetate = 1) | No Data |
| Vapor Pressure (mm-Hg @ 70oF) | No Data |
| Vapor Density (AIR = 1) | > 1 |
| Solubility in Water | Complete |
| Volatile Organic Compounds (VOCs) | 196 grams per liter or 20% by weight VOC's. |
| SECTION 10: Stability and Reactivity |
| Hazardous Polymerization – This product will not undergo hazardous polymerization. |
| Hazardous Decomposition or Byproducts – Carbon dioxide, carbon monoxide, hydrogen sulfide, sulfur dioxide, and soot. |
| Chemical Stability - Stable |
| Incompatibility (Materials to Avoid) - Strong acids, oxidizers, isocyanates, acetaldehyde, chlorine, ethylene oxide, aluminum at temperatures > 50o C (122o F) |
| SECTION 11: Toxicological Information |
| Isopropyl alcohol: Acute Dermal: LD50 >2000 mg/kg, Rabbit |
| Acute Oral: LD50 >2000 mg/kg, Rat |
| Acute Inhalation: LC50 >5000 ppm / 1 hour, Rat |
| SECTION 12: Ecological Information |
| Isopropyl alcohol: Fish LC50: >100 mg/L |
| Algae LC50: >1000 mg/L |
| SECTION 13: Disposal Consideration |
| Disposal Method - Dispose of in accordance with all applicable local, state, and federal regulations. |
| RCRA Waste Information – As packaged. if this product becomes a waste, it would not be a hazardous waste as defined by RCRA (40 CFR 261). The liquid concentrate would be considered a hazardous waste (D001). However the waste should be properly characterized to evaluate whether its composition has been modified prior to disposal. |
| SECTION 14: Transport Information |
| DOT Information – 49 CFR 172.101 |
| Proper Shipping Description: Not Regulated |
| Hazard Class: None |
| Identification Number: None |
| Packing Group: None |
| Marine Pollutants: None |
| SECTION 15: Regulatory Information |
| US Federal Regulations: |
| TSCA (Toxic Substances Control Act) Status |
| All ingredients are on the TSCA inventory or are not required to be listed on the TSCA inventory. |
| CERCLA RQ – 40 CFR 302.4 (a) |
| None Listed |
| SARA 313 Components – 40 CFR 372.65 |
| None |
| State and Local Regulations: |
| California Proposition 65 |
| Warning: This product contains a trace chemical (Ethylene Oxide; <0.25 ppm) known to the State of California to cause cancer and birth defects or other reproductive harm. |
| Section 16: Additional Information |
| Rev. 1 - 03/22/06 |
| WARNING! The use of this product is beyond the control of the manufacturer; therefore, no guarantee, expressed or implied, is made as to the effects of such or the results to be obtained if not used in accordance with directions or established safe practice. The user must assume all responsibility, including injury or damage, resulting from its misuse as such, or in combination with other materials. The manufacturer warrants only that this product meets the manufacturer's specifications for such product. THIS WARRANTY IS IN LIEU OF ALL OTHER WARRANTIES, EXPRESS OR IMPLIED, AS TO DESCRIPTION , QUALITY, MERCHANTABILITY. FITNESS FOR ANY PARTICULAR PURPOSE, PRODUCTIVENESS, OR ANY OTHER MATTER, OF THIS PRODUCT. THE MANUFACTURER SHALL BE IN NO WAY RESPONSIBLE FOR THE IMPROPER USE OF THIS PRODUCT. The sole and exclusive remedy against the manufacturer for breach of warranty shall be reimbursement of the purchase price of the product in the event that a defective condition of the product shall be found to exist. NO OTHER REMEDY (INCLUDING BUT NOT LIMITED TO INCIDENTAL OR CONSEQUENTIAL DAMAGES FOR INJURY TO PERSON OR PROPERTY OR ANY OTHER INCIDENTAL OR CONSEQUENTIAL LOSS) SHALL BE AVAILABLE. |